# Upgrade Procedure for Agilent Infiniium Oscilloscopes

This upgrade procedure is valid only for Agilent Infiniium models 54810A, 54815A, 54820A, 54825A, 54835A, 54845A, and 54846A.

- Locate the VIN # and Serial Number from the rear panel of the Infiniium oscilloscope.

- Look on the following table to see the initial hardware installed on that oscilloscope:

| Mobo | VIN # | CPU Speed | Available RAM | 3.5” Floppy Drive | Serial No. Prefix*** |
| --- | --- | --- | --- | --- | --- |
| AMI | VIN# (NONE)* | 100 MHz | 8 MB | Standard 1.44 MB |  |
| AMI | VIN# 015 | 100 MHz | 8 MB | Standard 1.44 MB | Less than US3810, no LAN card installed |
| AMI | VIN# 020 | 200 MHz | 8 MB | Standard 1.44 MB | All |
| AMI | VIN# 025 | 300 MHz | 64 MB | Standard 1.44 MB | Less than US3919, optical LS-120 not available |
| AMI | VIN# 025 | 300 MHz | 64 MB | Floptical 120 MB | US3919 and greater, optical LS-120 is standard |
| FIC | VIN# 030** | 400 MHz | 64 MB | Floptical 120 MB | US3949 – |
| FIC | VIN# 031** | 400 MHz | 64 MB | Floptical 120 MB |  |
| FIC | VIN# 032** | 400 MHz | 64 MB | Floptical 120 MB | – US4023 |
| FIC | VIN# 033 | 400 MHz | 64 MB | Floptical 120 MB | Higher |

*There is no VIN# on early Infiniium models

**Part of the recovery program needs upgraded

***The Serial No. Prefix is the first 6 characters of the serial number

- If the Infiniium oscilloscope has a VIN# 025, 030, 031, 032, or 033, and the Serial No. Prefix is US3919 or greater, then you may visit the following on-line software order page to obtain the latest software version:

http://software.cos.agilent.com/Infiniium

Note:  Because of the large size of the software upgrades, you must order the LS-120 disk for installation on your Infiniium oscilloscope.  Downloading the software would not be feasible.

- If the Infiniium oscilloscope does not meet the criteria listed in item 3 above, then you must purchase

the appropriate Infiniium performance upgrade listed below, and submit your oscilloscope to an

Agilent service center.  To order an upgrade, please call 1-800-829-4444.  To schedule an installation of an upgrade kit, please call 1-800-403-0801.

E2633-68701 is for Serial No. Prefixes lower than US3845……………………….....US $1500.00 ea.

This option includes all option 003 features, upgrading processor to 300 MHz, increasing RAM to 64 MB, adding a LAN card (if not already installed)

E2633-68703 is for Serial No. Prefixes from US3845 and up…………………………US $450.00 ea.

This option includes upgrading you oscilloscope to Windows 98 and the latest version of Infiniium software, replacing the 1.44 MB floppy drive with LS-120 SuperDisk 120 MB floptical, and other hardware adjustments and updates

Note:  An extra fee may be charged by the Agilent service center if a calibration or sound card

Installation for voice control is necessary.  The customer will pay for shipping the oscilloscope

to the service center, but not for return postage.